## Slide 1: IPC Example ex46_graph
Data Graph

## Slide 2: Introduction
This example performs on-demand loading of DSP processors and illustrates how to establish IPC communication.
The data graph provides a context for the concepts presented here. It is not a fundamental part of IPC.

## Slide 3: Overview
DSP Loading
  Fixed load order
  Load in any order – new support
The data graph
  Nodes and connections
  Demo
IPC Attach
  IPC Attach Modes
  Rules for attaching
  Attach examples

## Slide 4: Overview (continued)
The data graph
  IPC communication
  The Cluster Manager
IPC focus points and code examples
  Creating a new process
  Synchronizing startup between threads
  Synchronizing shutdown

## Slide 5: DSP Loading
Fixed load order
  Load all DSPs first
  Run host application
DSP1
DSP2
DSP3
DSP4
Program
Program
Program
Program
Program
IPC
Ipc_start
HOST

## Slide 6: DSP Loading
On-demand loading of DSP
  Load DSPs in any order
  Run host program first (or at an time)
DSP1
DSP2
DSP3
DSP4
Program
Program
Program
Program
Program
IPC
Ipc_attach
HOST
Ipc_start

## Slide 7: Data Graph
Nodes are fixed functionality
Producer
Consumer
Connections provide the IPC communication path
  IPC supports bi-directional communication
Consumer
Producer

## Slide 8: Data Graph
Data flows in the graph from a producer node to a consumer node.
  Arrow indicates data flow (not communication path).
Consumer
Transformer nodes operate on input data to generate new output data.
Producer
Transformer
Producer
Transformer
Consumer
Data
Data
Data'
Data''

## Slide 9: Data Graph
Data
Data
Combiner node receives two inputs and generates one output
Producer
Producer
Consumer
Combiner
Data

## Slide 10: Data Graph
The data graph supports multiple, independent streams
Transformer
Producer
Transformer
Consumer
Data
Data
Data
Transformer
Producer
Consumer
Data
Data

## Slide 11: Data Graph - Summary
The following table summarizes the data graph details.
  The nodes run on designated processors
 | Producer | Consumer | Transformer | Combiner
Processor | HOST | HOST | DSP | DSP
Execution Context | Process | Process | Global | Global
Input, Output | 0, 1 | 1, 0 | 1, 1 | 2, 1

## Slide 12: Graph Demo
The first example will be to build the following data stream. Note that both nodes are running on the HOST.
Producer
[HOST]
Consumer
[HOST]
Data

## Slide 13: Graph Demo
Now we will rebuild the data stream to include a transformer node running on the DSP.
Transformer
[DSP1]
Producer
[HOST]
Consumer
[HOST]

## Slide 14: Graph Demo
The next example is to add a second data stream which has two producers, two transformers, one combiner, and one consumer node.
Transformer
[DSP5]
Producer
[HOST]
Consumer
[HOST]
Transformer
[DSP6]
Producer
[HOST]
Combiner
[DSP8]

## Slide 15: IPC Attach Modes
IPC attach mode controls what happens in Ipc_start.
Two attach modes:
  Ipc.ProcSync_ALL – all processors attach at the same time
  Ipc.ProcSync_PAIR – each processor attaches explicitly
All processors must agree on the same attach mode.
Ipc.ProcSync_ALL
  All participating DSPs must be loaded and running first. They must all call Ipc_start at the same time.
  When the host program calls Ipc_start, it will implicitly attach to all running DSPs.
Ipc.ProcSync_PAIR
  DSPs and host programs can start in any order.
  Calling Ipc_start will *not* attach. You must call Ipc_attach explicitly from your program.

## Slide 16: IPC Attach Rules
You must always call Ipc_start before any other IPC API.
  On Linux, you must call Ipc_transportConfig before Ipc_start.
  On DSP, when Linux is running on the host, you must call IpcMgr_ipcStartup before Ipc_start.
You must attach before you can communicate with the remote processor.
You do not attach to yourself.
On Linux, call Ipc_attach for each DSP you communicate with.
When running on the DSP:
  You must attach to the owner of SR-Zero first (regardless). And the owner must attach to you at the same time.
  Attach to any additional DSP as needed. Both sides must attach to each other at the same time.
  You must call Ipc_attach in a loop. It takes several calls to work through the multi-stage handshake.

## Slide 17: IPC Attach Example
Linux program attach to DSP1
  DSP1 is SR-Zero owner
Linux program starts first
  Ipc_start
DSP1 program boots
  IpcMgr_ipcStartup
  Ipc_start
Linux attach to DSP1
  Ipc_attach
Ipc_transportConfig
Ipc_start
Start
load DSP1
IpcMgr_ipcStartup
Ipc_start
Ipc_attach(DSP1)
. . .
. . .
DSP1
HOST

## Slide 18: IPC Attach Example
Linux program attach to DSP3
  DSP1 is SR-Zero owner
Linux program already attached to DSP1
DSP3 program boots
  IpcMgr_ipcStartup
  Ipc_start
  Ipc_attach(DSP1)
Linux send attach command to DSP1 (attach to DSP3)
Linux attach to DSP3
  Ipc_attach
Start
load DSP3
Ipc_attach(DSP3)
. . .
. . .
DSP1
HOST
IpcMgr_ipcStartup
Ipc_start
. . .
DSP3
Idle
Ipc_attach(DSP1)
attach cmd
Ipc_attach(DSP3)

## Slide 19: IPC Attach Example
Start
load DSP4
Ipc_attach(DSP4)
. . .
. . .
DSP1
HOST
IpcMgr_ipcStartup
Ipc_start
. . .
DSP3
Idle
Ipc_attach(DSP1)
attach cmd
Ipc_attach(DSP4)
DSP4
Idle
attach cmd
Ipc_attach(DSP4)
Ipc_attach(DSP3)
. . .

## Slide 20: Data Graph – IPC Communication
MessageQ is used for all IPC communication in the data graph.
  Each node has a command queue for passing command messages.
  Each node has a data queue (reserved) for passing data messages.

## Slide 21: IPC Communication
A node input object is a MessageQ instance.
A node output object is a MessageQ QueueId.
Transformer
A
Producer
B
Consumer
C
Data
Data
HOST
DSP1
HOST
R: MessageQ
q: QueueId
n: MessageQ
Output
Command
R: MessageQ
q: QueueId
n: MessageQ
Output
Command
Input
R: MessageQ
n: MessageQ
Command
Input
empty
data
data
empty
data
data
Logical
Implementation
connect procId qIdx
run
pause
connect procId qIdx
(return)

## Slide 22: IPC Communication
Combiner needs only one input queue
Data
Data
Producer
Producer
Combiner
R: MessageQ
q: QueueId
Output
R: MessageQ
q: QueueId
Output
(return)
(return)
R: MessageQ
q: QueueId
Output
Input
data
data
data
data

## Slide 23: IPC Communication - summary
Data queues are reserved queues.
  Producer data queue is for return messages.
Command queues are named queues.
  Could also be reserved queues.
Use separate queues for data and commands.
Producer
R: MessageQ
n: MessageQ
Command
(return)
Transformer
R: MessageQ
n: MessageQ
Command
Input
Combiner
R: MessageQ
n: MessageQ
Command
Input
Consumer
R: MessageQ
n: MessageQ
Command
Input

## Slide 24: Cluster Manager
The Cluster Manager (CM) application is used to interact with the example. It accepts user input from the keyboard and issues commands.
  The CM issues system commands to run the loader (mpmcl).
  The CM uses IPC to send command messages to the nodes.
The console thread parses the user input and constructs a command object. The command is sent to the ClusterMgr thread using MessageQ.
The ClusterMgr thread receives all input from its message queue. This provides a consistent interface regardless of the message origin: user input, reply message, or asynchronous node message.

## Slide 25: Cluster Manager
manager
ClusterMgr
Console
n: MessageQ
NULL: MessageQ
STDIN
(reply)
Cmd_Command
Graph_Msg
Command
A message queue can receive multiple message types. Use the message ID to distinguish between the types.
The console thread sends Cmd_Command messages to the cluster manager thread.
The CM thread sends Graph_Msg messages to the nodes.

## Slide 26: Cluster Manager - example
manager
ClusterMgr
Console
n: MessageQ
NULL: MessageQ
(reply)
Command
A
Producer
R: MessageQ
n: MessageQ
Command
(return)
B
Consumer
R: MessageQ
n: MessageQ
Command
Input
q: QueueId
Output
launch consumer
launch producer
Cmd_Command
system("...")
stdin
connect A B
Graph_Msg

## Slide 27: Focus Point – new host process
Use fork and exec to run a new program
  ClusterMgr_sytem(char *cmd, bool wait)

## Slide 28: Focus Point – synchronizing startup
Your application has two threads which use IPC:
  Control Thread
  Pump Thread
The control thread will start IPC.
The pump thread must wait for the control thread to start IPC before it can create a message queue.
The control thread need not wait for the pump thread.
The control thread cannot assume that the synchronization object has been created.
create threads
initialization
Start
initialization
IPC startup
MessageQ_create
MessageQ_create
Control
Thread
Pump
Thread
Sync object created above
Continue
Continue

## Slide 29: Focus Point – synchronizing startup
Bool ipcReady = FALSE;
Bool okayToSignal = FALSE; int waitEvent = -1;
Pump_setup(...)
{
...
/* create event object */
waitEvent = eventfd(0, 0);
okayToSignal = TRUE;
/* wait here until IPC is ready */
if (!ipcReady) {
read(waitEvent, ...);
}
/* okay to create a message queue */
MessageQ_create(...);
}
Pump_ipcIsReady(void)
{
ipcReady = TRUE;
/* make sure if okay to signal */
if (okayToSignal) {
write(waitEvent, ...);
}
}
Pump.c
#include “Pump.h”
Control_Setup(...)
{
...
/* initialize IPC */
Ipc_transportConfig(...);
Ipc_start();
/* setup the transport module */
TransportPMQ_setup();
MessageQ_registerTransportId(...);
/* inform pump module that IPC is ready */
Pump_ipcIsReady();
/* create a message queue */
MessageQ_create(...);
}
Control.c

## Slide 30: Focus Point – synchronizing startup
This solution is still fallible.
If the control thread fails the initialization phase, the pump thread would wait forever on the synchronization object.
It is the control thread’s responsibility to abort the pump thread.
create threads
Start
initialization
signal failure
Abort
Abort
init failed?
yes

## Slide 31: Focus Point – synchronizing shutdown
The control thread will stop IPC.
The control thread must wait until the pump thread is finished using IPC.
The control thread will busy-wait.
  This avoids circular dependency.
  Avoids race with pump thread initialization timing.
Start
MessageQ_delete
MessageQ_delete
Pump_ipcDone()
IPC shutdown
ipcDone = TRUE
false
true
Stop
Stop

## Slide 32: Thank You!