## Slide 1: AIF2 LLD
Driver architecture for multiple software stacks
EMEA Telecom System Applications
Sebastien Tomas – Benjamin Mouchard

## Slide 2: SW stack needs for Cpri traffic
Different SW stacks need to access AIF2 resources simultaneously
  Lte, Wcdma, Ethernet fast C&M
AIF2 needs to be programmed at once during application initialization.
AIF2 has 2 DMA modes:
  DIO xor PKTDMA for Antenna IQ samples
  When applications co-exist on the same device, only one mode selected
  DIO recommended for Dual Lte/Wcdma Mode
  PKTDMA used for Ethernet fast C&M in any case
Different stacks can generate traffic for the same AIF2 link, or different ones.
  Antenna IQ and Cpri control words can be on the same link
Applications have also different timing needs
  That influences the programming of AIF2 radio timers
  AT events are also shared resources.
That implies that the different applications need a mechanism to describe their AIF2 resource needs, and in return, get access to a specific resource, for instance a Dio engine number, or a Pktdma/HW queue

## Slide 3: Current SW stack limitations
The current implementation of L1 stacks SW is interleaved with AIF2 configuration for CPRI link
  CPRI link setup procedure has been implemented as part of L1 SW
  It is performed after receiving FAPI PHY START message from L2
Such a startup sequence is creating following issues in the overall system
  CPRI link setup is dependent on L1 SW (not practical for a RRH)
  CPRI link is down whenever L1 SW suspends/crashes (should not be the case)
  Any reconfiguration/reset of L1 SW requires complete CPRI link setup/synchronization to be repeated and thus creating delays in reconfiguration/reset
LTE RRH case: from the overall eNB layers startup procedure the FAPI PHY START message is tied to Cell Setup trigger, so unless the Cell setup command is complete- L1 SW cannot come up which in turn shall enable the CPRI link and thus the Communication with Radio head cannot be started unless the Cell setup is complete. This essentially means that radio head software download, radio head configuration cannot be performed till cell setup is complete. Communication link with radio head is lost whenever L1 SW is down as the CPRI link is also down.

## Slide 4: Multi-stack scenarios of interest
Small cell Lte and Wcdma simultaneous traffic
  1 AIF2 4x link for Lte, 1 AIF2 4x link for Wcdma
  AIF2 DIO mode for both traffic
  AIF2 interfaces to FFTC, RAC,TAC, and DDR/SL2
Small cell Lte and Ethernet Fast C&M
  Same AIF2 4x link for both types of traffic
  AIF2 PKTDMA mode for both traffic
  AIF2 interfaces to FFTC and DDR/SL2

## Slide 5: Implementation proposal
De-couple AIF2 configuration from Lte and Wcdma L1 software
One instance of AIF2 LLD across all applications
  Place AIF_ConfigObj in shared memory section and let AIF2 LLD manage it
AIF2 register handling
  Centralized configuration and AIF2 exception monitoring
    Only one DSP core will perform the actual programming of AIF2 registers
    Only one DSP core manages AIF2 exceptions, and then need a notification/alarm mechanism to the different stacks
Application interfaces
  Init time
    AIF_ResDescObj describes in one structure the needs from all stacks (mode, link number, number of AxCs, dio engine number, …)
    Each stack gets the configuration during init time and is in charge of configuring its DMA parameters (PktDMA or DIO)
  Runtime
    Stacks get radio timer info thru specific lld APIs
    To push/pop/recycle packets, this is done thru qmss lld using fields from the AIF_ConfigObj
Sync points across all cores:
  For init/get resources from AIF_ResDescObj
  Prior to AIF_initHw()

## Slide 6: Architecture Diagram