## Slide 1: Fast c&m support
AIF2 driver architecture for Ethernet over CPRI
Sebastien Tomas, Piyush Patel

## Slide 2: Customer’s problem
We need to be able to communicate control information over Ethernet over CPRI interface to a remote radio. We would like to do it on Linux on the ARM processor core.
Is Ethernet over CPRI driver available on Linux? If not, is there a plan to supply the one and when? Is there any other way to it, like from the user space using some TI Libraries?

## Slide 3: Architecture diagram

## Slide 4: Usage Note 24: AIF2 CPRI Fast C&M Restrictions
http://www.ti.com/litv/pdf/sprz370b
This usage note describes some hardware (HW) limitation and restriction of the AIF2 Fast Ethernet CPRI control word channel operation. This includes one HW limitation about Fast Ethernet SSD (Start of Stream Delimiter) handling. This usage note also explains the HW restrictions of 4B5B encoded data nibble level swapping, hyperframe boundary delimitation and Ethernet packet CRC32 usage.
Chosen workaround in architecture diagram is:
  to implement the CRC + 4B5B encoder and decoder on ARM side, i.e. software implementation of Fast CM
  Transmit/receive data over AIF2 in a Null Delimiter mode
  Dsp example code for the workaround can be provided

## Slide 5: MsgCom references
DSP – ARM Communication requires the SysLib package from SC-MCSDK: http://software-dl.ti.com/sdoemb/sdoemb_public_sw/sc_mcsdk/2_01_00_01/index_FDS.html
Task on DSP core 0 is responsible for relaying packets from:
  MsgCom channel to AIF2 fast c&m Tx queue
  AIF2 fast c&m Rx queue to MsgCom channel