## Slide 1: KeyStone Interfaces: Programming with IQNet2
KeyStone Training
CI Hardware Applications

## Slide 2: Agenda
IQN2 Driver Overview
Support for Simultaneous Radio Standards
Driver APIs and Initialization Example
Synchronization Process and Exception Counters

## Slide 3: IQN2 Driver Overview
KeyStone Interfaces: Programming with IQNet2

## Slide 4: Software Overview
IQN2 LLD:
Configures IQN2 sub-blocks for the different modes of operation
Does NOT own PktDMA configuration and the associated Rx/Tx descriptor HW queues
Allows to have multiple SW entities running on ARM or DSP to push or pop packets to/from IQN2, each SW entity being in charge of configuring its separate Rx/Tx PktDMA channels
Does NOT configure SerDes and DFE blocks

## Slide 5: IQN2 Driver Architecture
IQN2 Device Driver:
  a set of well defined API
  a set of well defined OS abstraction API, used to ensure OS independence and portability.
  includes IQN2 functional layer for MMR accesses.
  executes on ARM Linux and DSP
  single instance driver, functional layer can be used on multiple cores for runtime adjustments

## Slide 6: IQN2 Driver: Key Features
IQN2 Functional Layer:
  Supports all IQN2 sub-blocks but PktDMA
  Includes AIL, Top, AID2, IQS2, DIO2, AT2, and all EEs
Single instance LLD driver:
  Runs on DSP or ARM (user mode)
  Several mode of operations:
    LTE, WCDMA, Dual mode, and Generic Packet mode*
    CPRI over AIL, including CPRI control words*
    OBSAI over AIL
    DFE over AID2 (AxC/CTL)
  * Not supported in initial release (1.0.0.0)

## Slide 7: IQN2 Driver Data Structures
IQN2_ConfigObj:
Exposes high level parameters to allow users to configure IQN2
Parameters such as the type of antenna traffic, the number of links, the protocol, the data width, the DMA mode etc…
Contains configuration objects for IQN2 sub-blocks such as AIL, DIO2, or AID.
Contains objects for Antenna Container (AxC), Radio Timer (RADT), and AT2 events.
References Iqn2Fl instance and the Iqn2Fl setup which are used to configure IQN2 HW

## Slide 8: Support for Simultaneous Radio Standards
KeyStone Interfaces: Programming with IQNet2

## Slide 9: Simultaneous Radio Standards (1)
AxC parameters provided are by the user application
The LLD:
  browses AxCconfig[] array
  creates new groups of contiguous AxCs objects with the same radio standard properties.
Up to 8 radio standards (groups) supported for up to 48 AxCs
baseGroupInfo_t
(internal to LLD)
samplingRate
cpType
startAxC
endAxC
isPopulated
isLte
IQN2_AxCObj
sampleRate
cpriPackMode
lteCpType
egressLteCellId
egressAxCOffset
ingressAxCOffset
inboundDataWidth
outboundDataWidth

## Slide 10: Simultaneous Radio Standards (2)
In IQN2_AilConfigObj and IQN2_AidConfigObj
  firstRdStdAxC determines the first index
  numRdStdEgress/IngressAxC for the number of AxCs
  RdStd=LTE or WCDMA
  These indexes correspond to AxCconfig[] entries
User application provides AxC numbers
  Different RdStd Axc index can’t overlap.
  For instance, if Wcdma AxCs are configured first
    firstLteAxC = firstWcdmaAxC + \ max(numWcdmaEgressAxC, numWcdmaIngressAxC)

## Slide 11: Simultaneous Radio Standards (3)
Separate application radio timers for DL and UL (up to 8)
  1 to 1 mapping between egress radio standards and radio timers.
  Default radio timer parameters are applied by LLD
  Override of the default parameters supported (userSpecified=1)
    For LTE
      number of LTE symbols per symbol strobe is configurable
      number of LTE symbols per frame strobe as well.
      allows an LTE application to work at 1-symbol pace, or 2-symbol pace, etc …
RADT parameters | Default values
initFrameLsbNum | 1
initFrameMsbNum | 0
frameTerminalCount | 4096
bcnCompValue | 0
Frame strobe | Every 10ms, so: LTE: 140 symbols (default is normal CP) WCDMA: 15 slots
Symbol strobe | Every symbol, so: LTE: every symbol with normal CP WCDMA: every slot (2560 chips)

## Slide 12: Simultaneous Radio Standards (4)
Up to 24 AT2 event objects in the LLD
  used by SW applications, EDMA channels, and hardware accelerators as system events for CPU interrupts, transfer triggers, or hardware processing ticks
AT2 event0 is connected to the EXTFRAMEEVENT external pin and can be used to synchronize with external test equipment.
AT2 event8 is dedicated for the RAC, AT2 event 9 for TAC.
Events linked to one of the radio timers, hence radio standard.
Applications need to:
  specify the radio timer id, and the type of strobe (symbol/frame), along with offset and modulo values.
  offset and modulo values are expressed in byte clock unit, but user applications can first express those in nanosecs and get a conversion to byte clocks with LLD API

## Slide 13: Driver APIs and Initialization Example
KeyStone Interfaces: Programming with IQNet2

## Slide 14: IQN2 Functional Layer
Functional layer public APIs
IQN2 Functional Layer | Description
Iqn2Fl_init | Peripheral specific initialization function
Iqn2Fl_open | Opens an instance of iqn2 fl
Iqn2Fl_hwSetup | Initializes the device registers
Iqn2Fl_hwControl | Controls IQN2 operation based on the control command
Iqn2Fl_getHwStatus | Gets IQN2 status values based on the status query command
Iqn2Fl_close | Closing an instance of iqn2 fl

## Slide 15: IQN2 Driver APIs
Driver public APIs
IQN2 Driver | Description
IQN2_calcParameters | Calculates IQN2 timing and delay parameters according to the pre-set parameters in IQN2_ConfigObj.
IQN2_initDio | Sets up the dio configuration structure given the application parameters.
IQN2_initHw | Sets up the IQN2 FL setup structures given the IQN2_ConfigObj instance
IQN2_startHw | Configures IQN2 HW registers given user IQN2 configuration. HW is then started, waiting for the selected synchronization
IQN2_runBcnTimer | Starts the BCN Timer free running. SW writes are not precise so it is expected in real case system, the application SW will correct the timer value with an offset. IQN2_resyncProcedure is used up on a resync external event.
IQN2_initRadioTimer | Sets up the IQN2 FL setup Radio Timer structures given the IQN2_ConfigObj instance, and the egress/ingress radio standards configured during IQN2_initHw().
IQN2_initAt2Event | Sets up the IQN2 FL setup AT2 event structures given the IQN2_At2Eventobj instance. This instance is also registered in IQN2_ConfigObj instance.
IQN2_enableAt2Event | Enables a given AT2 event, assuming this event was already initialized
IQN2_disableAt2Event | Disables a given AT2 event
IQN2_getIngressRadioStandardId | Returns the ingress radio standard ID associated with the AxC
IQN2_getEgressRadioStandardId | Returns the egress radio standard ID associated with the AxC. Used for dynamic control of MBSFN in LTE
IQN2_getIngressRadioTimerId | Returns the ingress radio timer ID associated with the AxC number. Ingress radio timer id is equal to Ingress radio standard id + max number of populated radio standards. Application may need to have separate radio timers for downlink and uplink. Following call to IQN2_initHw(), with this function, the application can get a radio timer ID and pass user-specified parameters for radio timers in IQN2_ConfigObj
IQN2_getEgressRadioTimerId | Returns the egress radio timer ID associated with the AxC number. Egress radio timer id is equal to Egress radio standard id. Application may need to have separate radio timers for downlink and uplink. Following call to IQN2_initHw(), with this function, the application can get a radio timer ID and pass user-specified parameters for radio timers in IQN2_ConfigObj.
IQN2_enableException | Configures IQN2 HW registers to enable errors at alarms at IQN2 level
IQN2_resetException | Resets IQN2LLD exception counters
IQN2_captureException | Captures the exception counts into a supplied destination storage
IQN2_resetIqn2 | Used to reset IQN2 to its default state

## Slide 16: Initialization example

## Slide 17: Agenda
Introduction to IQN2
  Albert’s part
How to Program with IQN2 Driver
  Driver overview
  Support for simultaneous radio standards
  Driver APIs and initialization example
  Synchronization process, Exception counters

## Slide 18: Synchronization Process Exception Counters
KeyStone Interfaces: Programming with IQNet2

## Slide 19: Synchronization Process (1)
The AT2 module in IQN2 hardware can detect synchronization from an external source. The possible synchronization sources include:
    RP1 FCB packet
    Rad sync input pin
    Phy sync input pin
    Pa_tscomp sync input from NETCP PA (IEEE1588 sync)
SW intervention required to achieve radio frame synchronization

## Slide 20: Synchronization Process (2)
SW procedure is described in chapter 7.3.3.2 of the KeyStone II Architecture IQN2 User Guide.
Implemented in IQN2_resyncProcedure().
Requires waiting for several radio frames in between some of the IQN2 timers adjustments, hence the requirement for the user application to implement the Osal_iqn2Sleep() callback with 1 to 2ms sleep time.
Overall resynchronization procedure is expected to take around six 10-ms radio frames.

## Slide 21: Exception Counters
Enabling the IQN2 exception handling.
  IQN2_enableException() used to enable all IQN2 events at once.
  Separate exception enable functions for all IQN2 modules
    Allows to choose which interrupt event to use for each IQN2 module.
    InterruptEventNum could be set to 0 (EV0) or 1 (EV1).
Monitoring exception flags
  IQN2_getException() increments the counters
    Can be called from a CPU interrupt, or called periodically.
    First checks the exception origin registers and flags
  Individual module exception functions exists
IQN2_captureException (): snapshot of the current exception counters
Exception counters can be reset by calling IQN2_resetException().

## Slide 22: For More Information
For more information, refer to the KeyStone II Architecture IQNet2 User Guide
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.