## Slide 1
This work is licensed under a Creative Commons Attribution-Share Alike 4.0 (CC BY-SA 4.0)
GENIVI is a registered trademark of the GENIVI Alliance in the USA and other countries
Copyright © GENIVI Alliance 2016
Vehicle Signal
Specification
2016-08-30
Magnus Feuer
Head System Architect | Expert Group Lead
Jaguar Land Rover

## Slide 2: The Problem
GENIVI is a registered trademark of the GENIVI Alliance in the USA and other countries
Copyright © GENIVI Alliance 2016
Vehicle state is being off boarded to Internet services
There is no standard / process that fits the bill
No public forum where changes can be processed in a lightweight manner
One format does not suit all
Decouple IVI from electric architecture

## Slide 3: VSS - Introduction
GENIVI is a registered trademark of the GENIVI Alliance in the USA and other countries
Copyright © GENIVI Alliance 2016
Standardizing signal specification
YAML subset
Minimum attributes
Lightweight change process
Single source – multiple targets
Feed other standardization organizations (W3C, etc)
Technically simple

## Slide 4: VSS Signal structure

## Slide 5: Naming Convention
Body.Mirror.Left.Heated
Body.Mirrors.Right.Heated
Cabin.Door.Row1.left.open
Cabin.Door.Row2.left.open
Dot notated name path
Last component is signal or attribute

## Slide 6: Specification source format: Branches
- Transmission:
type: branch description: Transmission-specific data, stopping at the drive shafts.
YAML list
Only type and description mandatory

## Slide 7: Specification source format: Signals
- Speed:
type: Uint16
unit: km/h
min: 0
max: 350
description: Vehicle speed
Uses Franca typing
Optional interval
Optional SI unit type
Can be enumerated

## Slide 8: Specification source format: Attributes
- Weight:
type: Uint16
unit: kg
default: 1485
description: Vehicle weight
Signal with a default value
Used to describe configuration data

## Slide 9: Signal source format
Multiple files aggregated together to a uniform specification
YAML-compliant include directives used to aggregate spec fragments
Facilitates git(hub) working model
Minimizes commit conflicts
root.vspec
VSS spec
nav.vspec
engine.vspec
ivi.vspec
root.vspec
#include engine.vspec
#include nav.vspec
#include ivi.vspec

## Slide 10: Spec file re-use
YAML-compliant include directives used to aggregate specification fragments
An update to a fragment is propagated to all locations where it is used
Facilitates git(hub) working model
root.vspec
Cabin
Door
Row1
Row2
Left
Locked
WinPos
Open
Locked
WinPos
Open
Right
Locked
WinPos
Open
Right
Locked
WinPos
Open
Left
door.vspec
#include door.vspec Cabin.Door.Row1.Right
#include door.vspec Cabin.Door.Row1.Left
#include door.vspec Cabin.Door.Row2.Right
#include door.vspec Cabin.Door.Row2.Left
- Locked: …
- WinPos: …
- Open: …

## Slide 11: Private Extensions
A proprietary signal specification can use the GENIVI VSS as a starting point
Can be used in production project to integrate with vendors
Mature private extensions can be submitted for VSS inclusion
Body
Teleport
IVI
Power
AntiGravity
oem_x_proprietary.vspec
#include vss_23.vspec
- Private.OEM_X.AntiGravity.Power: …
- Private.OEM_X.TSeleport.TargetLoc: …
…
Engine
....
Private
OEM_X
…
TargetLoc
…
vss_23.vspec
oem_x_proprietary.vspec

## Slide 12: Overriding signal definitions
vss_23.vspec
oem_x_proprietary.vspec
Original specification lacks "semi-auto" mode in gearbox.
OEM-specific vspec file can override the original signal and redefine it.
vss_23.vspec
GearChangeMode: enum: [ "auto", "manual" ]
Drivetrain
GearChangeMode
enum: [ "auto", "manual" ]
oem_x_proprietary.vspec
#include vss_23.vspec
GearChangeMode: enum: [ "auto", "manual", "semi-auto" ]
Transmission
Drivetrain
GearChangeMode
enum: [ "auto", "manual", "semi-auto" ]
Transmission

## Slide 13: Declaring and Defining Attributes
vss_23.vspec
oem_x_proprietary.vspec
Declaration is done as GENIVI-official VSS attribute with a nil default
Declaration is overridden by definition in OEM/project-specific spec file with correct value
Attribute
vss_23.vspec
Chassis.Weight: value: 0
Engine.Displacement value:0
Chassis
Engine
Weight:
value:0
Displacement
value: 0
Attribute
Chassis
Engine
oem_x_proprietary.vspec
#include vss_23.vspec
Chassis.Weight: value: 1580
Engine.Displacement value:3198
Weight:
value:1580
Displacement
value: 3198

## Slide 14: Generating target specifications
root.vspec
Markdown
Specification
VSS parser
nav.vspec
engine.vspec
ivi.vspec
Markdown
generator
FrancaIDL
generator
JSON
generator
FrancaIDL
Specification
JSON
Specification
Parser loads and interprets specification files
Generators produces target documents and specifications
Targets can be used as input to production projects and other organizations
Additional generators can be added as needed.
…
…

## Slide 15: Release management
PR#1
V1
master
Pull requests submitted by anyone
Mail discussion on genivi-projects list to approve request into develop branch
Develop branch merged into master prior to tagged release
Major number changes when existing tree structure is changed
V2
V3
V4
develop
Mail thread
PR#2
Mail thread
PR#3
Mail thread
PR#4
Mail thread
PR#5
Mail thread
x

## Slide 16: More Info
github.com/PDXostc/vehicle_signal_specification
Demo time